## Slide 1: Literature Review -
End-to-end Learning and Reinforcement Learning in Obstacle Avoidance

## Slide 2: End-to-end learning with image input
End-to-End Driving via Conditional Imitation Learning (2018): At training time, the model is given not only the perceptual input and the control signal, but also a representation of the expert’s intention.
Link: https://arxiv.org/abs/1710.02410
Notes: A vehicle trained end-to-end to imitate an expert cannot be guided to take a specific turn at an upcoming intersection.

## Slide 3: End-to-end learning with image input
Off-Road Obstacle Avoidance through End-to-End Learning (2005): using two cameras as input of the neural network.
End-to-End Deep Learning for Autonomous Navigation of Mobile Robot (2018): regular methods of using single image. Nothing original.
Vision-Based Mobile Robot Navigation through Deep Convolutional Neural Networks and End-to-End Learning (2017): Nothing original.
CNN-Based Vision Model for Obstacle Avoidance of Mobile Robot (2017): Nothing original.

## Slide 4: End-to-end learning with laser scan input
A LIDAR based end to end controller for robot navigation using deep neural network (2017): A sliding window of past information is incorporated to add the memory to controller, so that the hesitation is reduced when ambiguity occurs.
Link: https://ieeexplore.ieee.org/document/8278417/

## Slide 5: End-to-end learning with laser scan input
The target information is a combination of the last three frames of target information. Then they would be inserted into fully-connected layers to output the control commands.

## Slide 6: End-to-end learning with laser scan and images input
LIDAR-Video Driving Dataset: Learning Driving Policies Effectively (2018): a dataset which is the first policy learning benchmark composed of driving videos, LIDAR data and corresponding driving behaviors.
DNN + LSTM. Long short-term memory (LSTM) is a well-improved recurrent neural network by introducing memory gates.
Depth representation: Point Clouds Mapping: LIDAR points are divided into grids on XOZ plane and we could get the nearest points of Y coordinate in each grid. PointNet: It directly take disorder pointes as the input of neural networks and finally output the representation features.
Vehicle speed and steering angle prediction models are trained individually.

## Slide 7
Link: http://openaccess.thecvf.com/content_cvpr_2018/html/Chen_LiDAR-Video_Driving_Dataset_CVPR_2018_paper.html

## Slide 8: End-to-end reinforcement learning with laser scan input
Virtual-to-real Deep Reinforcement Learning: Continuous Control of Mobile Robots for Mapless Navigation (2017): taking LIDAR data and target position as input and steering commands as output. Using asynchronous DDPG method.
Notes: The original DQN could only be used in tasks with a discrete action space. To extend it to continuous control, deep deterministic policy gradients is proposed. Asynchronous deep=RL with multiple sample collection threads working in parallel would improve the training efficiency. The increasing of Q-value of ADDPG is much faster.

## Slide 9: End-to-end reinforcement learning with laser scan input
Reward function definition
Link: https://ieeexplore.ieee.org/document/8202134/
Notes: Otherwise, the reward is the difference in the distance from the target compared with last time step, multiplied by a hyper-parameter.

## Slide 10: Reinforcement learning with image input
Towards Monocular Vision based Obstacle Avoidance through Deep Reinforcement Learning (2017): a dueling architecture based deep double-Q network is proposed, using only monocular RGB vision.
Link: https://arxiv.org/abs/1706.09829
Notes: In the dueling network, two streams of fully connected layers are built to compute the value and advantage functions separately, which are finally combined together for computing Q-values.

## Slide 11: Reinforcement learning with image/laser scan input
Uncertainty-Aware Reinforcement Learning for Collision Avoidance (2017): presenting an uncertainty-aware model-based learning algorithm that estimates the probability of collision together with a statistical estimate of uncertainty.
The collision prediction model is a fully connected neural network (policy gradient method).
Inputs are current state, the sensor observation, and a sequence of controls.
Outputs are the probability of collision, the uncertainty which is the variance, and a collision cost which is used in MPC.
In order to obtain accurate uncertainty, they use two techniques: bootstrapping and dropout.
Notes: This learning method would proceed cautiously, experiencing only low-speed collisions until it gains confidence.

## Slide 12: Reinforcement learning with image/laser scan input

## Slide 13: Reinforcement learning with image/laser scan input
Link: https://arxiv.org/abs/1702.01182
Notes: Each iteration of the algorithm, the cost function C is formed using the current uncertainty-aware collision prediction model. The model predictive controller then samples trajectories using cost C. These sample trajectories are aggregated into a dataset containing all previous sampled trajectories. Then the collision prediction model is trained on the dataset according to Alg.1 and the next iteration begins.

## Slide 14: Reinforcement learning
Motion Planning Among Dynamic, Decision-Making Agents with Deep Reinforcement Learning (2018): an algorithm that learns collision avoidance among a variety of types of dynamics agents without assuming they follow any particular behavior rules. It is a kind of modified actor-critic method.
Neural networks based reinforcement learning for mobile robots obstacle avoidance (2016): providing mobile robots a collision-free trajectory within an uncertain workspace which contains both stationary and moving entities. It is a modified Q-Learning approach.

## Slide 15: Reinforcement learning
End-to-End Race Driving with Deep Reinforcement Learning (2018): including hand brake command in the learning algorithm to enforce drifting. An Asynchronous Actor-Critic framework is used. RGB Image input.
Avoiding Moving Obstacles with Stochastic Hybrid Dynamics using PEARL: PrEference Appraisal Reinforcement Learning (2016): PEARL projects the high-dimensional continuous robot state space to a low dimensional preference feature space resulting in efficient and adaptable planning.
Notes: They trained the agent with 4 static obstacles, while the trained agent avoids up to 900 moving obstacles.